## Slide 1: Implementation and simulation in TinkerCAD
Implemented the architecture and two of our basic use cases in TinkerCAD
  Acceleration of emergency vehicles
  Smart street lighting
Used Arduino Unos as a hardware platform for the Traffic Manager and the End Nodes

## Slide 2: Overview of the simulation
Simulation replicates a simple street intersection with four arms
Traffic Manager is located in the middle
Four End Nodes that are located in every direction
The camera for recognizing entities is resembled by:
  PIR sensor for detecting approaching citizens that want to cross straight ahead
  Button for approaching emergency vehicles
The traffic light and the street lights are resembled by LEDs
Communication between the Traffic Manager anf the End Nodes via I2C

## Slide 3: Overview of the simulation
Intersection is working in a fixed-time mode after starting up
Every direction has a green signal for 15s by default
Events:
Citizen that wants to cross the intersection detected:
  Street lights are turned on for 15s
Approaching emergency vehicle signs up:
  Intersection switches to a green light as fast as possible and holds the state
Emergency vehicle signs off after crossing:
  Intersection continues normal operation
Notes: Intersection is working in a fixed-time mode after starting up
Every direction has a green signal for 15s by default
Three events that influence the behavior:
Citizen that wants to cross the intersection straight ahead detected:
Street lights of the opposite arm are turned on for 15s
Approaching emergency vehicle signs up (via wireless telegram in real life):
Intersection switches to a green light as fast as possible and holds the state
Emergency vehicle signs off after crossing:
Intersection continues normal operation

## Slide 4: Implementation of the Traffic Manager
Functionality was divided into four tasks:
T1: Communication via I2C
  P1 = 100ms, WCET(T1) = 2152us
T2: Logic of traffic lights of the intersection
  P2 = 1s, WCET(T2) = 40us
T3: Displaying status of the system
  P3 = 2s, WCET(T3) = 29512us
T4: Controlling the street lighting
  P4 = 1s, WCET(T4) = 212us
Notes: Task 1:
  Transmitting messages that are waiting in a buffer
  Polling values of sensors
Task 2:
  Controlling the status of the traffic lights
  Taking approaching emergency vehicles into account
  Sequence implemented via a FSM
  Switch case state machine with guarded transitions
Task 3:
  Displaying the status of the system via serial outputs
Task 4:
  Turning on the street lights for 15s when a citizen is detected that crosses the intersection straight ahead

## Slide 5: Implementation of the Traffic Manager
Implemented a rate-monotonic scheduler without preemption
  Created a struct called “Task” that contains the attributes:
    ID
    Period (in ms)
    Execution time (measured duration in us)
    Last execution time (timestamp)
    Function pointer to the task’s function
  Scheduler uses a “task set” consisting out of an array of tasks
  Method “runRMS” needs to be called in the main loop; decides which task needs to be executed next, executes it, measures execution time and updates the last execution time
  Preemption is not supported
Notes: Some words about the most interesting part: implemented a rate-monotonic scheduler without preemption
First created a struct called “Task” that contains the attributes:
  ID
  Period (in ms)
  Execution time (measured duration in us)
  Last execution time (timestamp)
  Function pointer to the task’s function to know what needs to be executed
Scheduler uses a “task set” consisting out of an array of tasks
Method “runRMS” needs to be called in the main loop, decides which task needs to be executed next, executes it, measures execution time and updates the last execution time
Preemption is not supported because it was not needed to implement the example and would have

## Slide 6: Implementation of Traffic Manager
Way of implementation and the separation resulted in clean code
Implementation of the scheduler made it easy and fast to add new tasks
Periodicity was utilized by task 2 and 4 to implement a counter to count seconds (used for guarded transitions)
Functions of the tasks needed to be designed carefully not to block the whole system
Lack of preemption removed the need of locking mechanisms
Notes: To conclude a little on the implementation of the Traffic Manager:
The implementation of the scheduler resulted in a suprisingly clean code (clean in terms of what is normally archievable on an Arduino)
For example : Task 4 (functionality of the street lights) was added after the traffic lights; effort payed off
Periodicity was utilized by task 2 (logic of the traffic lights) and task 4 (control of the street lights) to implement a counter for seconds used for the guarded transitions in the SM and the timers of the street lights. Measurements showed it to be surprisingly precise.
Because the scheduler implements no preemption, the tasks needed to be designed in a non-blocking way
Lack of preemption removes the need of locking mechanisms: shared resources are not accessed in a concurrent way