## Slide 1: SmartCity

## Slide 2: Requirements
Specification of every case scenario for the smart city.
Each case scenario needed it requirements.
More attention was given to the case scenario to implement.

## Slide 3: Case Scenario
Emergency Vehicles going through an intersection.
Implementation of the the basic use case that was going to be implemented.

## Slide 4
Intersection controlled by a traffic manager.
Traffic Lamps are end nodes.
  Receive current state.
  Transmit if emergency vehicle is detected.

## Slide 5: Traffic Manager
One Manager will control each intersection.
One Manager will communicate with city system to coordinate.

## Slide 6: Traffic Lamp
Definition of the components inside the traffic light.

## Slide 7: Lightning System
Definition of the components inside the traffic light.

## Slide 8: Internal State Machine
Definition of the most basic state machine of a traffic light.
Refinement of the state machine to accommodate our use case scenario.

## Slide 9: Sequence Diagrams
Definition for 2 use cases.
  Emergency Vehicles
  Non-Emergency Vehicles
Refinement of the sequence diagrams to fit a correct behavior.

## Slide 10: Implementation and simulation in TinkerCAD
Implemented the architecture and two of our basic use cases in TinkerCAD
  Acceleration of emergency vehicles
  Smart street lighting
Used Arduino Unos as a hardware platform for the Traffic Manager and the End Nodes

## Slide 11: Overview of the simulation
Simulation replicates a simple street intersection with four arms
Traffic Manager is located in the middle
Four End Nodes that are located in every direction
The camera for recognizing entities is resembled by:
  PIR sensor for detecting approaching citizens that want to cross straight ahead
  Button for approaching emergency vehicles
The traffic light and the street lights are resembled by LEDs
Communication between the Traffic Manager anf the End Nodes via I2C

## Slide 12: Overview of the simulation
Intersection is working in a fixed-time mode after starting up
Every direction has a green signal for 15s by default
Events:
Citizen that wants to cross the intersection detected:
  Street lights are turned on for 15s
Approaching emergency vehicle signs up:
  Intersection switches to a green light as fast as possible and holds the state
Emergency vehicle signs off after crossing:
  Intersection continues normal operation
Notes: Intersection is working in a fixed-time mode after starting up
Every direction has a green signal for 15s by default
Three events that influence the behavior:
Citizen that wants to cross the intersection straight ahead detected:
Street lights of the opposite arm are turned on for 15s
Approaching emergency vehicle signs up (via wireless telegram in real life):
Intersection switches to a green light as fast as possible and holds the state
Emergency vehicle signs off after crossing:
Intersection continues normal operation

## Slide 13: Implementation of the Traffic Manager
Functionality was divided into four tasks:
T1: Communication via I2C
  P1 = 100ms, WCET(T1) = 2152us
T2: Logic of traffic lights of the intersection
  P2 = 1s, WCET(T2) = 40us
T3: Displaying status of the system
  P3 = 2s, WCET(T3) = 29512us
T4: Controlling the street lighting
  P4 = 1s, WCET(T4) = 212us
Notes: Task 1:
  Transmitting messages that are waiting in a buffer
  Polling values of sensors
Task 2:
  Controlling the status of the traffic lights
  Taking approaching emergency vehicles into account
  Sequence implemented via a FSM
  Switch case state machine with guarded transitions
Task 3:
  Displaying the status of the system via serial outputs
Task 4:
  Turning on the street lights for 15s when a citizen is detected that crosses the intersection straight ahead

## Slide 14: Implementation of the Traffic Manager
Implemented a rate-monotonic scheduler without preemption
  Created a struct called “Task” that contains the attributes:
    ID
    Period (in ms)
    Execution time (measured duration in us)
    Last execution time (timestamp)
    Function pointer to the task’s function
  Scheduler uses a “task set” consisting out of an array of tasks
  Method “runRMS” needs to be called in the main loop; decides which task needs to be executed next, executes it, measures execution time and updates the last execution time
  Preemption is not supported
Notes: Some words about the most interesting part: implemented a rate-monotonic scheduler without preemption
First created a struct called “Task” that contains the attributes:
  ID
  Period (in ms)
  Execution time (measured duration in us)
  Last execution time (timestamp)
  Function pointer to the task’s function to know what needs to be executed
Scheduler uses a “task set” consisting out of an array of tasks
Method “runRMS” needs to be called in the main loop, decides which task needs to be executed next, executes it, measures execution time and updates the last execution time
Preemption is not supported because it was not needed to implement the example and would have

## Slide 15: Implementation of Traffic Manager
Way of implementation and the separation resulted in clean code
Implementation of the scheduler made it easy and fast to add new tasks
Periodicity was utilized by task 2 and 4 to implement a counter to count seconds (used for guarded transitions)
Functions of the tasks needed to be designed carefully not to block the whole system
Lack of preemption removed the need of locking mechanisms
Notes: To conclude a little on the implementation of the Traffic Manager:
The implementation of the scheduler resulted in a suprisingly clean code (clean in terms of what is normally archievable on an Arduino)
For example : Task 4 (functionality of the street lights) was added after the traffic lights; effort payed off
Periodicity was utilized by task 2 (logic of the traffic lights) and task 4 (control of the street lights) to implement a counter for seconds used for the guarded transitions in the SM and the timers of the street lights. Measurements showed it to be surprisingly precise.
Because the scheduler implements no preemption, the tasks needed to be designed in a non-blocking way
Lack of preemption removes the need of locking mechanisms: shared resources are not accessed in a concurrent way

## Slide 16: Implementation and Testing in Tinkercard
Created the code and hardware connections for the End Node
Created the Unit Tests for the project

## Slide 17: The End Node Components
The lights for the traffic lights
The digital signal button
The PIR Sensor for detecting movement
The lights for the road
The Arduino for the end node

## Slide 18: The End Node Functionality
Receive signals from the Manager to turn on/off the traffic lights
Receive signals from the Manager to turn on/off the road lights
Send an emergency signal to the manager with the digital button is clicked
Send a movement signal when movement is detected from the PIR sensor
Send an emergency signal when the digital button is clicked

## Slide 19: Testing the code
Tests were written in C++ (same language as Arduino)
4 unit cases were tested
The tests covered ideal cases & defected cases
The functions/code for the tested cases were copied from the Tinkercard environment into the testing environment (the function.cpp file)

## Slide 20: Tested the End Node Signal Handler
Tested all possible valid signals from the manager to the end node
Tested invalid signals from the manger to end node
Test if end node updates as needed

## Slide 21: Tested the addPacketTX() function
This is function from the Traffic Manager Code
Tested adding a value packet to the buffer
Test trying to add an invalid packet to the buffer

## Slide 22: Tested task1_communication() function
This is function from the Traffic Manager Code
The function is meant to send signals from the traffic manager to the end nodes & Receive the emergency and road lights signal from them
In the test environment the function was split into 2 to simplify debugging and testing